## Cara setting TP-LINK TLWA601

Setting Access Point dengan Merk TP-LINK seri TL WA601 G, :

Setting Client, (update berikutnya tentang AP buat hotspotan)

- Ubah IP komputermu menjadi 192.168.17.2 dengan subnet mask 255.255.255.0

cara mengubahnya : control panel -> network connection -> Local Area Network -> properties -> TCP/IP -> properties

- Buka web browser kemudian ketik 192.168.1.1 (ini IP default Radio tersebut) dan masukan user : admin, pass : admin

- Pilih menu wireless kemudian pilih basic setting

- Pilih client dan masukan SSID dan MAC yang anda maksudkan, apabila anda belum yakin dengan nama SSIDnya anda bisa mencarinya lewat tombol surver yang berada di paling bawah menu, namun sebelumnya perlu di ingat untuk memilih option client terlebih dahulu

- klik tombol survey.

- Klik tombol connect

- Kembali ke awal menu dan centang pilihan reboot, kemudian klik tombol save.

Membuat Hot Spot dirumah dengan Access Point TP-Link TL-WA601G

Membuat hotspot menggunakan HP Nokia N95 saya bisa konek ke Internet di rumah,

Peralatan :

- Acces Point TP-Link seri TP-WA601G

- Kabel UTP +RJ45

- Komputer/Laptop yang ada LanCardnya

Langkah-langkahnya :

- Colokan kabel UTP dari radio ke Kompi/Laptop

- Masuk ke Radionya

- Isi IP Komputer =   IP Address    : 192.168.1.2
                                  Subnet Musk : 255.255.255.0

- OK dan Close

- Buka Browser Internet, isi Address : 192.168.1.1 (enter)

- Isi User : admin

- Password : admin

Setelah masuk ke radio, di menu sebelah kiri cari :

- Wireless

- Basic Settings

- Ganti SSID misal “Paijo Hot Spot Free”

- di Access Point = centang Enable SSID Broadcast

- centang Reboot

- Save

- Tunggu booting beberapa saat

- Copot kabel UTP di kompi

- Colokin ke sumber internet misal Sapidy Personal

- Search dengan SmartPhone, PDA, Laptop dan siap Browsing

- Selesai

2. Change the LAN IP Address of the Wireless Repeater

The default LAN IP address of TL-WA501G/TL-WA601G is 192.168.1.1. So if the LAN IP of the remote AP or wireless Router is 192.168.1.1 too, you¡¯d better change the LAN IP address of TL-WA501G/TL-WA601G to avoid IP Conflict.

That is, if the LAN IP of the remote AP or Wireless Router isn¯t 192.168.1.1, you don¡¯t need do

anything in this step, please skip to next step.

Step 1: Open the web browser and type the LAN IP address of the router in the address bar, the default IP address of TP-LINK router is 192.168.1.1, and then press Enter.

Step 2 Type the username and password in the login page, the default username and password both are admin in lower case.

Step 3: Click Network on the left, change the LAN IP address in the IP Address field. Then press the Save button to reboot the Access Point and Enable the new IP address.

Note:

The IP address should be in the range of the same subnet with your wireless router. The Subnet mask should be 255.255.255.0; the default gateway is the same with your gateway device (such as wireless router)¡¯s IP address which is usual192.168.1.1.

3. Set up Repeater Mode on TL-WA501G/ TL-WA601G

Note: Before we set up the Access Point to Repeater mode, please make sure the remote AP or wireless router is powered on and working normally.

After login the web-based utility of TL-WA501G/TL-WA601G by using the new IP address, we can set the Access Point as Repeater Mode now.

Step 4: Click Wireless -> Basic Settings on the left of the page, select the Repeater. If the wireless router which you want to repeat is not supporting WDS we can enable Universal Repeater.

Step 5: Click Survey Button in the bottom of the page.

Then it will find the SSID of Wireless Routers in the AP list. Select the SSID of your own Wireless Router and click connect.

Step 6: Select Reboot and Click the Save button in the page of Basic Settings to save your settings. Then the router will reboot and repeat the signal of your wireless router automatically.

Step 7: Make your wireless connection to ¡°Obtain an IP address automatically¡± and then detect the signal of your wireless router and connect it.

Step 8: Check the wireless connection, if it is shown similar as following picture, congratulation, now you have extended the range of your wireless network.

How to configure TCP/IP Properties of my computer to connect to TP-LINK wireless router?

Suitable for : TL-WR941N/TL-WR841N/TL-WR642G/TL-WR641G/TL-WR543G/TL-WR542G/TL-WR541G/TL-WR340G

Here we take Windows XP as an example, and please make certain that your Ethernet Adapter is working well.

Step 1 On the Windows taskbar, click the Start->Control Panel, then select and double-click Networking Connections.

Step 2 Right Click Local Area Connection, select and click Properties.

Step 3 Select Internet Protocol (TCP/IP), then double click it or click Properties.

Step 4 The TCP/IP Properties window will display, there are two ways to configure the TCP/IP Properties, automatically or manually.

1. Assigned automatically by DHCP server

Select Obtain an IP address automatically and even Obtain DNS server address automatically if necessary, then click OK to save the settings.

2. Assigned manually

Select Use the following IP address, type IP address, subnet mask and default gateway IP address into it.

Select Use the following DNS server addresses, type your local area DNS server IP addresses into it.

Step 5 Click OK to save and apply your settings.

Note:

1.  The IP address should be in range of 192.168.1.2 to 192.168.1.253, you can use anyone of them. The Subnet mask should be 255.255.255.0; the default gateway is usual 192.168.1.1 which is the same with your router¡¯s IP address.

2.  The DNS server addresses are provided by your ISP, please contact with your ISP to check them.

How do I renew an IP address for my computer?

Suitable for : Windows 2000/XP/2003/Vista

If you had configure your computer as Obtain an IP address automatically, some times such as after you change the IP address of your router, then you need renew the IP address of your computer to access the network/router.

1. For Windows 2000/XP/2003

Step 1 Click Start->Run, type cmd and press Enter.

Step 2 Type ipconfig /release at the prompt window, press Enter, it will release the current IP configuration.

Step 3 Type ipconfig /renw at the prompt window, press Enter, wait for a while, the DHCP server will assign a new IP address for your computer.

2. For Vista

Step 1 Click Start on the task bar, type cmd into the search box and press Enter.

Step 2 Type ipconfig /renew at the prompt window, wait for a while, the DHCP server will assign a new IP address for your computer.